## Slide 1: Themes of Carbonate Oil field Complexity Issaran Field November 2021
12API, 1000-3000cP dual porosity fractured carbonate; Steam-EOR
High well density and high data density

## Slide 2
Carbonate reservoirs are in general more complex than sandstone reservoirs
Heterogeneity
Aeolian
Clastics
Tidal
Clastics
Shallow
Marine
Clastics
Dual porosity
Carbonates
Issaran

## Slide 3: Dual Porosity Behaviour at field scale: Qarn Alam Oilfield, PDO Oman
the oil contained in the highly permeable fracture network was produced and replaced mostly by formation water
Same is true for the Nukhul in Iss
From: Penney et all 2007
SPE 105406

## Slide 4: Resolving Carbonate Reservoir Complexity – Issaran Identified Themes
The depositional Environment
Flow Unit identification
Understanding Diagenetic processes
Petrophysical Complexity
Fracture Modelling
New Technology implementation
To tackle this complexity, a structured and theme-based approach is required
Reservoir properties are dependent on primary depositional factors and secondary diagenetic processes
Significant niche expertise is essential

## Slide 5: Issaran Identified Themes – Depositional and Facies Heterogeneity
High Anhydrite Percentage (>60%)
Low Anhydrite Percentage (<20%)
in carbonate reservoirs, original depositional architecture can be key in the prediction of petrophysical properties.
Anhydrite Probability based on 100 wells; 1 by 3 km

## Slide 6: Issaran Identified Themes – Depositional and Facies Heterogeneity
Geological Model
Facies distribution extracted from inverted seismic data Model
Inverted Seismic Data
High Anhydrite Percentage (>60%)
Low Anhydrite Percentage (<20%)
High Anhydrite Probability
Low Anhydrite Probability
ISS-41
2020 reprocessing by WesternGeco
Also inversion done in 2021
Broad similarity provides predictive power; I-233

## Slide 7: Issaran Identified Themes – High Resolution Flow unit Identification
Flow Unit-01
Flow Unit-02
UDD
UDC
Enhanced Oil Recovery means injecting money into the reservoir (Hi P gas, polymers or steam)
Understanding baffles and barriers is key for well design (horizontal vs deviated or vertical as well as Steam WRM

## Slide 8: Issaran Identified Themes – Diagenetic Heterogeneity
Fractures filled with minerals
Fossils replacement by Dolomite and-or Anhydrite
In carbonate reservoirs, the original depositional architecture can be overprinted by later diagenetic effects.
Cementation, dissolution, compaction, dolomitization and fracturing are normal diagenetic impacts in carbonate reservoirs.
It can completely modify the depositional K/PHI properties.
Dissolution of fossils high porosity
And no change in permeability

## Slide 9: Issaran Identified Themes – Diagenetic Heterogeneity
AFR taken in every well is key
Niche expertise in HLB Cairo great help

## Slide 10: Issaran Identified Themes – Diagenetic Heterogeneity
Dissolution
Vugs “ 2-3 ft.”
Dissolution and mineralization filled fracture
2 ft
Disseminated Dissolution
Vugs “ 0.1 ft.”
The heterogeneity is driven by diagenetic and depositional processes
It creates a triple heterogeneity in the Issaran Upper Dolomite:
    Matrix porosity
    Fracture porosity
    Vuggy porosity
Image log acquisition is essential
No Acid no steam this well produced 150bopd May-Aug

## Slide 11: Issaran Identified Themes – Fracture Modelling
Upper Dolomite Block G
Consistent image log data acquisition and interpretation
Integrate structural model with fracture data
Develop a model for the nature of the fractures and variability over the field
Extrapolate the fracture system into the inter-well area

## Slide 12: Issaran Identified Themes – Fracture Modelling
Upper Dolomite Block G
Well on Steam
Nearby Production well
With 4 days response
Group steam strategy

## Slide 13: Issaran Identified Themes – Petrophysical Complexity
Typical poro-perm relationship in clean sandstone and carbonates
From: Arwini 2020
Clastic systems in general have reasonable poro-perm relationships.
In carbonates there is often little or no relationship between porosity and permeability.
The underlying reason is pore size distribution, which can vary over very short distances in carbonates owing to the irregularity of pore shapes.
Interwell prediction
Rate, Oil charge and OWC

## Slide 14: Issaran Identified Themes – new technology implementation
14
Identify
Electric
DH Heaters
Define
Select
Execute
Hzl
Drilling
w/ Frac
USRD
GOGD
TA-GOGD
Isolation
Packer
Gas/Heat
Solvent
AICVs
Anhy
Dissolver
Water
Pumpoff
ESPCP
CSI
GCCS
CSS
Acid Frac/
HF Pilot
Foam
Steam
Cement
Remedial
GHG
Monitor
Heavy Oil
Carbonate Reservoir
Fractured Reservoir
Steam EOR
Microseismic
Frac Maps
BFD
(Bio)
Anhydrite
from Inversion

## Slide 15: Conclusions
Theme based approach to tackle Carbonate Reservoir Complexity is essential to provide focus
Clear Technical and commercial objectives need to be defined for each study theme
    Reduce subsurface uncertainty by improved flow unit definition
    Optimise recovery from Upper and Lower Dolomite Reservoirs
      Improve modelling of permeability in carbonates
      To establish HiRes architecture of carbonate reservoirs in terms of flow paths and barriers
      Relate seismic response to reservoir quality
      Make a step-change in well productivity through piloting new Technology
𓏙 𓇋𓄿𓎡𓏲𓀘𓈉 𓎯𓏪
Stone that give Oil